## Slide 1: SmartX Labs for Computer Systems
Box Lab v09
(2016, Spring)
NetCS Lab

## Slide 2
History and Contributor of Box Lab
(2016. 04. 27)
Version | Updated Date | Updated Contents | Contributor
v01 | 2015/09 | OvS, Docker 자료 초안 작성 | 배 정 주
v02 | 2015/09 | KVM 자료 초안 작성 | 윤 희 범
v03 | 2015/10 | 자료 취합 및 Functions Lab 초안 제작 | 배 정 주
v04 | 2015/10 | Functions Lab 자료 편집 및 수정 | 윤 희 범
v05 | 2016/03 | Function Lab → Box Lab 이전 작업, 세부자료 수정 | 남 택 호
v06 | 2016/04 | 추가 설명자료 및 단어 교정, History 작성 | 남 택 호
v07 | 2016/04 | Outline 추가, 검수자 피드백 반영 | 남 택 호
v08 | 2016/04 | 실습 중 발생한 이슈에 대한 개선사항 추가 (docker container command, if configuration 충돌) | 남 택 호
v09 | 2016/06 | 불필요한 Prerequisite 제거, Appendix 추가 (mirror site 변경코드 제거) | 남 택 호 김 병 돈

## Slide 3
Box Lab: Outline
em1
br0
VM
Container
Tap1
ping test

## Slide 4: Virtualization: Basic Concept
Tenant A Virtual
Network
Tenant B Virtual
Network
Tenant C Virtual
Network
Any Physical Network
(Packet Forwarding)
Network Virtualization

## Slide 5
http://bradhedlund.com/2013/05/28/what-is-network-virtualization/
Virtualization is the basic act of decoupling an infrastructure service from the physical assets on which that service operates. With the virtual network fully decoupled, the physical network configuration is simplified to provide packet forwarding service from one hypervisor to the next
Virtualization: Basic Concept

## Slide 6
VM
Box Lab: Final Goal

## Slide 7
Open vSwitch: Goal of this part
- Update and Configuration

## Slide 8
A switch for every server means a 50:1 (virtual : physical) ratio; Approaching feature-­parity with hardware switches: Visibility, ACLs, Quality of Service; Optionally leveraging hardware oﬀ-loading
Tight integration with hypervisor  Good for virtual edge (e.g., inter-VM) networking, network overlay: the leading initial NV use case
Centralized management
VMWare, Nicira (open & proprietary), Cisco, IBM, Microsoft
  VMware vSwitch (vDS), Cisco Nexus 1000V, Open vSwitch
vSwitches: Virtual(soft) Switches

## Slide 9
H/W Switches: With an approach like pass through + tagging + switching in the NIC (with enforcement in the first hop switch); Latency is reduced to the wire speed; Packet classification noticeably outperforms x86-based software switches.
S/W Switches: Flexibility and upgrade cycle of software + Benefits of virtualization (memory overcommit, page sharing, etc.); Simple resource efficiency
  Can saturate a 10G link from a guest to the wire with less than a x86 CPU core (assuming MTU size packets), Can saturate a 1G link with less than 20% of a core. In the case of Open vSwitch, these numbers include full packet lookup over L2, L3 and L4 headers.
Virtual Switches: Soft vs Hardware

## Slide 10
Hypervisor
VM
Virtual switch
VM
VM
VM
Physical switch
Virtual NIC
Virtual
interface
Virtual L2 network
Virtual Switch: Basic Architecture

## Slide 11
http://openvswitch.org/
Open vSwitch: Introduction

## Slide 12
Openvswitch_mod.ko
ovsdb-­‐server
User Kernel
Control Cluster
Oﬀ-­‐box
ovs-­‐vswitchd
Management Protocol (6632/TCP) OpenFlow (6633/TCP)
Netlink
Open vSwitch: Main Components

## Slide 13
Open vSwitch: All Components

## Slide 14
Installed 64bit Ubuntu 14.04 LTS in Intel NUC
(We recommend to use desktop version)
Prerequisite for Box Lab

## Slide 15
Prerequisite for Box Lab
$sudo vi /etc/network/interfaces
----------------- /etc/network/interfaces -----------------
auto lo
iface lo inet loopback
auto eth0
iface eth0 inet static
address [ip address]
netmask [subnet mask]
gateway [gateway]
dns-nameservers [DNS nameserver]
----------------------------------------------------------------------------
$sudo ifdown eth0
$sudo ifconfig eth0 down
$sudo ifup eth0
Do not check ‘Enable Networking’
15

## Slide 16: OpenVswitch - Update & Install
$sudo apt-get update
$sudo apt-get install openvswitch-switch
Update index information of Open vSwitch package.
Install a Open vSwitch package, openvswitch-switch.
Other dependencies are automatically installed.

## Slide 17
Open vSwitch
- Basic command (ovs-vsctl)
$sudo ovs-vsctl add-br <bridge_name>
$sudo ovs-vsctl add-port <bridge_name> <NIC>
$sudo ovs-vsctl add-port <bridge_name> <port_name>
$sudo ovs-vsctl del-br <bridge_name>
$sudo ovs-vsctl del-port <port_name>
Example)
※You don’t need to follow below command.
$sudo ovs-vsctl add-br br0
$sudo ovs-vsctl add-port br0 eth0
$sudo ovs-vsctl add-port br0 po_to_anotherBr
eth0
br0
eth0
br0
po_to_anotherBr

## Slide 18
Open vSwitch
- Interface configuration setting
eth0
br0
Example)
※You don’t need to follow below command.
$sudo ifconfig eth0 0
$sudo ifconfig br0 0
$sudo ifup br0
$sudo ifconfig br0 up
$sudo ifconfig br0 203.237.x.x
$sudo ifconfig eth0 up
ip : 203.237.x.x
eth0
br0
ip : 0
ip : 203.237.x.x

## Slide 19: Open Vswitch - Configure bridged networking
Modify network interface configuration.
$sudo vi /etc/network/interfaces
----------------- /etc/network/interfaces -----------------
# The primary network interface
auto (eth0->)br0
iface (eth0->)br0 inet static
…
before
After

## Slide 20: Open Vswitch - Configure bridged networking
$sudo ovs-vsctl add-br br0

## Slide 21: Open Vswitch - Configure bridged networking
$sudo ovs-vsctl add-port br0 eth0
eth0 인터페이스가 global 영역에서 bridge 영역으로 이동하기 때문에 연결이 끊김

## Slide 22: Open Vswitch - Configure bridged networking
$sudo ifconfig eth0 0 // IP of eth0 → None
$sudo ifconfig br0 0 // IP of br0 → None
$sudo ifup br0 // interface br0 turn on
$sudo ifconfig br0 up // interface br0 turn on
$sudo ifconfig eth0 up

## Slide 23: Open Vswitch - Situation
Your Box
Your Box
eth0
0
br0
203.237.x.x
eth0
203.237.x.x

## Slide 24: Open Vswitch - Goal of this section
Your Box
eth0
br0
203.237.x.x
VM
203.237.x.x
Stop OvS setting, Now need to build KVM

## Slide 25: Modify - /etc/rc.local
$sudo vi /etc/rc.local
ifconfig eth0 up
Modify /etc/rc.local
Whenever NUC is rebooted,
interface configuration is initialized
by executing commands in rc.local

## Slide 26
VM
KVM: Goal of this part

## Slide 27
KVM (for Kernel-based Virtual Machine) is a full virtualization solution for Linux on x86 hardware containing virtualization extensions (Intel VT or AMD-V). It consists of a loadable kernel module, kvm.ko, that provides the core virtualization infrastructure and a processor specific module, kvm-intel.ko or kvm-amd.ko.
Using KVM, one can run multiple virtual machines running unmodified Linux or Windows images. Each virtual machine has private virtualized hardware: a network card, disk, graphics adapter, etc.
KVM is open source software. The kernel component of KVM is included in mainline Linux, as of 2.6.20. The userspace component of KVM is included in mainline QEMU, as of 1.3.
What is KVM?

## Slide 28: KVM - install dependency to upgrade KVM
$sudo apt-get install qemu-kvm libvirt-bin //upgrade KVM //qemu is open-source emulator
$wget http://releases.ubuntu.com/14.04.3/ubuntu-14.04.3-server-amd64.iso
(official)
//If above URL is can’t be downloaded, try below URL(dropbox link)
$wget https://www.dropbox.com/s/v6pwrksl9xdnvux/ubuntu-14.04.3-server-amd64.iso
(dropbox link, recommended)
Install dependency & download Ubuntu 14.04.3 64bit server image.
Now we are ready to make VM. So continue the setting.

## Slide 29: Open Vswitch - Configure bridged networking
Your Box
eth0
br0
203.237.x.x
VM
203.237.x.x
[tap_name]
This tap device will be attached VM. You can think this tap as a NIC of VM.
$sudo ip tuntap add mode tap [tap_name]
$sudo ifconfig [tap_name] up
$sudo ovs-vsctl add-port br0 [tap_name] // Turn on and attach to br0
Make a tap and attach to VM.
[tap_name]

## Slide 30: KVM - Prepare for Ubuntu VM
Make a VM image.
Boot VM image from Ubuntu iso file (mac should be different from others).
Download VNC viewer to see inside of VM
Windows : https://www.dropbox.com/s/h2mr0g8obm5mgpe/vncviewer.exe?dl=0
Ubuntu : sudo apt-get install xvnc4viewer
sudo kvm -m 512 -name tt -smp cpus=1,maxcpus=1 -device virtio-net-pci,netdev=net0,mac='EE:EE:EE:EE:EE:77' -netdev tap,id=net0,ifname=vport_vFunction,script=no -boot d vFunction20.img -cdrom ubuntu-14.04.3-server-amd64.iso -vnc :5 -daemonize
$sudo qemu-img create [img_name].img -f qcow2 [storage_capacity]
$sudo kvm -m [memory_capacity] -name [vm_name] -smp cpus=[#cpu],maxcpus= [#maxcpu] -device virtio-net-pci,netdev=net0,mac= [EE:EE:EE:EE:EE:EE] -netdev tap,id=net0,ifname= [tap_name],script=no -boot d [img_name].img -cdrom ubuntu-14.04.3-server-amd64.iso -vnc :[#] -daemonize

## Slide 31: KVM - Install Ubuntu to VM
IP address:vnc number
ex) 210.203.x.x:5

## Slide 34
public address

## Slide 36
Gateway ip of your public network

## Slide 37
Google DNS server

## Slide 38
Push esc

## Slide 39: KVM - VM boot command
If you want boot VM again (mac should be different from others).
$sudo kvm -m [memory capacity] -name [name] -smp cpus=[#cpu],maxcpus= [#maxcpu] -device virtio-net-pci,netdev=net0,mac= [EE:EE:EE:EE:EE:EE] –netdev tap,id=net0,ifname= [tap_name],script=no -boot d [name].img -vnc : [#] -daemonize

## Slide 40: Open Vswitch connects with KVM - Situation
eth0
br0
ip : 0
ip : 203.237.x.x
VM
tap_name
ip : 203.237.x.x

## Slide 41: Open Vswitch connects with KVM - Situation
eth0
br0
ip : 0
ip : 203.237.x.x
VM
tap_name
ip : 203.237.x.x
gateway: br0’s IP

## Slide 42: KVM - Don’t forget to install ssh in VM!
In VMs,
$sudo apt-get update
$sudo apt-get install ssh

## Slide 43
$sudo vi /etc/rc.local
ip tuntap add mode tap [tap_name]
ifconfig [tap_name] up
ovs-vsctl del-port br0 [tap_name]
ovs-vsctl add-port br0 [tap_name]
Modify /etc/rc.local
Modify - /etc/rc.local
Whenever NUC is rebooted,
interface configuration and OvS ports are initialized
by executing commands in rc.local

## Slide 44
Docker: Goal of this part

## Slide 45
Docker is an open platform for building, shipping and running distributed applications. It gives programmers, development teams and operations engineers the common toolbox they need to take advantage of the distributed and networked nature of modern applications.
What is Docker ?

## Slide 46
$sudo wget -qO- https://get.docker.com/ | sh
$sudo service docker start
$sudo adduser [your_id] docker
(Session restart)
$sudo docker run hello-world
reference: http://docs.docker.com/linux/step_one/
Docker - Installation
Docker installation.

## Slide 47
Docker - Installation

## Slide 48
Docker - Make containers
$sudo docker run -it --net=none --name [container_name] ubuntu /bin/bash
Run docker container.
I want to make interface that has 203.237.x.x IP address.
※ctrl + p, q  detach docker container
※docker attach [container_name]  get into docker container console

## Slide 49
Pros
  Easy to use
Cons
  Security problem (Violate docker’s strong point:isolated)
Solution?
  Establish L2 tunneling (Can easily achieved by using ovs. However, ovs doesn’t support raspberry pi officially. That’s why we are using this option.) Related keyword : GRE, vlan, vxlan
Docker - About [--net host] option

## Slide 50
Docker - Connect docker container to ovs bridge
$cd /usr/bin
$sudo wget https://raw.githubusercontent.com/openvswitch/ovs/master/utilities/ovs-docker
$sudo chmod a+rwx ovs-docker
$sudo ovs-docker add-port br0 eth0 [containerName] --ipaddress=[IP_address/24] --gateway=[Gateway_address]
$sudo docker attach [containerName]
#apt-get update
#apt-get install net-tools
#apt-get install iputils-ping
Install ovs-docker utility in host machine. (Not in inside of Docker container.)

## Slide 51: Modify - /etc/rc.local
$sudo vi /etc/rc.local
docker start [container_name]
ovs-docker del-port br0 eth0 [containerName]
ovs-docker add-port br0 eth0 [containerName] --ipaddress=[IP_address/24] --gateway=[Gateway_address]
Modify /etc/rc.local
Whenever NUC is rebooted,
network configuration of Docker container is initialized
by executing commands in rc.local

## Slide 52
Docker - Check connectivity

## Slide 53
KVM VM
Docker container
Docker connect with KVM - Check connectivity

## Slide 54
VM
Box Lab: Final Goal

## Slide 55: Appendix

## Slide 56
NUC OS Setting

## Slide 57: NUC OS Setting
BIOS Setting (64bit OS 설치시 필요)
  Booting 후 F2 버튼을 통해 BIOS Setting 화면으로 접속
  UEFI boot 체크 해제, (Legacy 방식으로 부팅)

## Slide 58: NUC OS Setting
OS : Ubuntu Desktop 14.04.4 LTS(64bit)
  Download Site : http://www.ubuntu.com/download/desktop
    OS 설치를 위해 download 된 파일(ubuntu-14.04.4-desktop-amd64.iso, 0.99Gb)을 이용하여 bootable USB 구성(bootable CD 는 불가능, NUC에 CD-Rom이 없음)
    NUC에 설치
설치 완료 후 Ubuntu 초기화면

## Slide 59: NUC & Pi2 IP address Setting
Pi2 IP address 설정을 위해 필요한 파일(편집은 root 만 가능)
  /etc/network/interfaces
  일반적으로 dns-nameservers 를 입력하면 9 page 는 필요 없으나, Hypriot OS 는 삽입되지 않으므로 resolv.conf 파일에 직접 nameserver를 입력해야 함!
$cd /etc/network
$sudo vi interfaces
#iface eth0 inet dhcp  # 은 주석
auto eth0
iface eth0 inet static
address 172.29.0.X  ip address
netmask 255.255.255.0  subnet mask
gateway 172.29.0.254  Gateway
dns-nameservers 203.237.32.100 203.237.32.101
입력 예

## Slide 60: NUC & Pi2 IP address Setting
Pi2 IP address 설정을 위해 필요한 파일
  /etc/resolv.conf
$cd /etc/
$sudo vi resolv.conf
$sudo /etc/init.d/networking restart 입력 또는 rebooting 후 network 확인
$sudo reboot (rebooting command)
# nameserver config
nameserver 203.237.32.100
nameserver 203.237.32.101
기존의 nameserver는 #을 추가하여
주석처리

## Slide 61: NUC & Pi IP address Setting
Network icon
Edit Connection.. 선택
NUC IP address Setting
  Pi와 동일하게 진행
  GUI 환경에서 setting
System Setting icon

## Slide 62: Linux Setting(NUC & Pi)
Ubuntu & Hypriot OS : Debian 계열 linux
  Package 관리 관련 명령어(apt-get : Advanced Packaging Tool)
    Update package index 갱신(/etc/apt/sources.list)
    Package 목록을 비교하여 package upgrade 실행
    Package 간의 의존성 검사를 하며 upgrade(optional)
  Package 설치(/var/cache/apt/archive/에 설치)
  자신에 맞는 기본적인 package 설치
    Kernel Lab(Pi2)을 위한 package : gcc-4.9, make
    Editor : vim(vi iMproved), emacs, gedit, etc.
    SSH(Secure Shell) : openssh
$sudo apt-get update
$sudo apt-get upgrade
$sudo apt-get dist-upgrade
$sudo apt-get install <package_name>

## Slide 63: Linux Beginner Guide
Terminal 창
< 간단한 명령어 모음 >
$pwd : 현재위치
$cd : Change directory
$ls : directory 보기
$mkdir : directory 생성
$su : root 계정으로 이용
$apt-get : package 설치 및 삭제
$poweroff
$shutdown –h now
eecs@eecs:~$
user
hostname
home directory

## Slide 64: Linux Beginner Guide
gcc-4.9 설치(NUC & Pi2)
  gcc 설치
  gcc version 확인 :
  NUC 에 gcc 설치를 위해 아래의 command 실행
$sudo apt-get install gcc-4.9
$gcc --version
< NUC >
< pi2 >
$sudo add-apt-repository ppa:ubuntu-toolchain-r/test
$sudo apt-get update
$sudo apt-get install gcc-4.9

## Slide 65: Linux Beginner Guide
gcc-4.9 설치(NUC & Pi2)
  version 확인
  link 설정을 해주면 된다.

## Slide 66: Linux Beginner Guide
gcc-4.9 link 설정
  현재 gcc-4.8 version 이 link 되어 있음
  현재의 link 를 지우고 4.9 version으로 재설정
$sudo rm /usr/bin/gcc : link 삭제
$sudo ln –s /usr/bin/gcc-4.9 /usr/bin/gcc : link 설정

## Slide 67: Vi/vim editor 명령어 모음
입력 모드 : 원하는 글자를 입력
  : 현재 위치의 다음부터 입력 시작
  : 현재 위치의 앞에서부터 입력 시작
명령 모드 : 문서 편집을 할 수 있으며, 입력 모드 상태에서 ESC키를 누르면 명령모드로 전환됨
  : 커서가 있는 문자 삭제
  : 현재 줄 전체 삭제
라인 모드 : ESC 키를 누른 후 colon(:) prompt 에서 명령을 입력하며 저장, 편집, 검색 기능 제공
  : 그대로 종료하기
  : 변경된 내용을 저장하지 않고 종료하기
  : 변경된 내용을 저장하고 종료하기
보다 다양한 명령어가 있으며, 직접 실습을 하는 것이 좋은 방법
a
i
:q
:q!
:wq
x
dd

## Slide 68
Thank You for
Your Attention
Any Questions?