## Slide 1
Computer Systems
For AI-inspired Cloud
Theory & Lab.
https://github.com/SmartX-Labs/SmartX-Mini-MOOC
Lab #4: IoT

## Slide 2
IoT Lab: Concept
Raspberry Pi Box
for IoT Sensors
& Actuators
Tower Box
for IoT-Cloud Service Visualization
NUC Box
for IoT-Cloud Hub
Temperature/Humidity Sensor data
Web Server Function
Sensor control message
Box provisioning / visibility
Data Transfer Function
Docker
Runtime
Data Capture Function

## Slide 3
Theory

## Slide 4
SmartX IoT-Cloud Services with Micoservices-based SaaS Applications
Machine containers
application containers
Process containers
(Monster containers)
VM hypervisors
p(Baremetal)
+ c(Container)
+ v(VM)

## Slide 5
Open-Source-leveraged Playgrounds
(IoT-SDN/NFV-Cloud (HPC/BigData) Ready)
SmartX
Open Playgrounds

## Slide 6: Smart Air IoT-Cloud Services over SmartX Open Platform
KOREN SmartX Platform을 활용한 선택된 산업인터넷 도메인에 대한 서비스 실증: 컨테이너 기반 Smart Air IoT-Cloud 서비스
Smart Air IoT-Cloud 서비스: 스마트폰
1) 스마트 폰에 연결된 먼지센서에서 발생한 데이터와 GPS값을 Apache Kafka
Producer를 통해 Data Lake로 전송
2) 스마트 폰에서 촬영한 영상 데이터 RTMP 기반 비디오 스트리밍
IoT-Cloud 대응형
SDN/Cloud 기반의 관제타워
SmartX Control Room 내의
타일드 디스플레이 기반의 가시화
Smart Air IoT-Cloud 서비스: Drone
동적 IOT 대시보드 구현
1) GRAFANA를 통한 데이터 가시화
2) InfluxDB를 통한 데이터 DB 연동
3) Timeshift를 이용한 실시간 데이터 표시
4) 다양한 패널들을 이용한 가시성 향상
데이터 가시화 웹 구현
1) Bootstrap기반 가벼운 웹 구축 및 Bootstap.js 활용
2) Nginx 기반 반응 Theme 활용
3) 편리한 디자인으로 사용성 개선
Smart Air IoT-Cloud 서비스 Dashboard
1) 종단 자원의 토폴로지/상태 정보 수집 및 가시화
2) OpenStack Neutron 네트워크 토폴로지 정보 가시화
3) ONOS SDN 제어기의 토폴로지 정보 가시화
1) SmartX Playground의 인프라와 서비스의 효과적인 관제를 위한 Control Room 구축
2) GIST 사이트 내에 위치한 타일드 디스플레이를 이용한 모니터링 지원
Smart Air IoT-Service Visualization

## Slide 7
Node.js Web Server Programming
Web
Server
(Daemon/
Service)
Server-side Script
(JSP, PHP, ASP, …)
Database
Web Browser
Client-side Script
(Java Script)
Web Browser
Client-side Script
(Java Script)
Web Browser
Client-side Script
(Java Script)
Web Browser
Client-side Script
(Java Script)
Server-side JavaScript
Database
Web Browser
Client-side Script
(Java Script)
Web Browser
Client-side Script
(Java Script)
Web Browser
Client-side Script
(Java Script)
Web Browser
Client-side Script
(Java Script)
Node.js Pros: Server-side JavaScript  High productivity; Single thread, non-block I/O  light-weight and agile; no direct I/O  no process blocking
Node.js Cons: Single thread  Complicated multi-process management for multi-core CPU efficiency; Overlapped event callback  callback hell; Memory management overhead due to Garbage Collection

## Slide 8: SmartX IoT-Cloud Services for Smart Energy Domain
IoT Concentrator
SDN Switch Agent
IoT Concentrator
IoT Gateway
IoT-Optimized
SDN Controller
Conv. Box Agent
Conv. Box Agent
SDN Virtual Switch
SDN Virtual Switch
VM
VM
Container
VM
VM
Container
Connectivity Manager
Input Adapter
I-CDN Agent
CEP Framework
DPI Framework
I-CDNQ
IoT Concentrator
IoT Gateway
IoT Core
G/W, Core
Lifecycle Manager
I-CDN Manager
IoT Orchestration
DashBoard
IoT Orchestration
Cloud Orchestration
IoT Service, Processor
API endpoint
DPI
Executor
IoT Service, Analyzer
API endpoint
EQL
Executor
Ops Tower
IoT Core
CEP
IoT Concentrator
IoT Concentrator
Cloud Orchestration
IoT SDN Controller
IoT Gateway
I-CDN
DevOps Tower Resources
Data Lake
Smart Energy IoT-Cloud Services for Mini Data Center
Control & Management
IoT-Cloud Hub
Data Collection / Validation
Mini DataCenter
Sensors
&
Actuators
Dev Tower
Docker Orchestration
IoT Concentrator
Lifecycle Manager
Application Visualization
Smart Energy Orchestration
IoT Orchestration
I-CDN Manager
IoT SDN Controller
I-CDN

## Slide 9
Practice

## Slide 10: NAME: NUC5i5MYHE (NUC PC) CPU: i5-5300U @2.30GHz CORE: 4 Memory: 16GB DDR3 HDD: 94GB
#0 Lab Preparation (1/2)
Wired connection
NAME: Raspberry Pi Model B (Pi) CPU: ARM Cortex A7 @900MHz CORE: 4 Memory: 1GB SD Card: 32GB
NAME: netgear prosafe 16 port gigabit switch(Switch) Network Ports: 16 auto-sensing 10/100/1000 Mbps Ethernet ports
NAME: NT900X3A
CPU: i5-2537U @1.40GHz
CORE: 2 Memory: 4GB DDR3 HDD: 128GB

## Slide 11
#0 Lab Preparation (2/2)

## Slide 12
IoT Lab: Concept
Raspberry Pi Box
for IoT Sensors
& Actuators
Tower Box
for IoT-Cloud Service Visualization
NUC Box
for IoT-Cloud Hub
Temperature/Humidity Sensor data
Web Server Function
Sensor control message
Box provisioning / visibility
Data Transfer Function
Docker
Runtime
Data Capture Function

## Slide 13
#1-1 Docker Container for Node.js Web Server: Run Container
Run a Docker Container
  $ sudo docker run –it –-net=host --name=webserver lshyeung/smartx_webserver
On container
  $ apt-get update
  $ apt-get install vim

## Slide 14
Open Server code and change NUC IP
  $ vi ~/SmartX-mini/IoT-labs/webserver.js
#1–2 Docker Container for Node.js Web Server: Server code

## Slide 15
Execute webapp.js
  $ cd SmartX-mini/IoT-labs
  $ nodejs webserver.js
Open browser and go to
  http://{IP_of_your_NUC}
#1–3 Docker Container for Node.js Web Server: Execute Server

## Slide 16
Download package from github
  $ git clone https://github.com/adafruit/Adafruit_python_DHT.git
Install package
  $ cd Adafruit_python_DHT
  $ sudo apt-get update
  $ sudo apt-get install python3-pip
  $ sudo python3 -m pip install --upgrade pip setuptools wheel
  $ sudo python3 setup.py install
#2–1 Temperature / Humidity Sensor test on Raspberry PI: Install package

## Slide 17
#2–2 Temperature / Humidity Sensor test on Raspberry PI: Sensor test
Move to example directory
  $ cd ~/Adafruit_python_DHT/examples
Modify test code (Change python to python 3)
  $ sudo vi AdafruitDHT.py
Execute test code
  $ sudo ./AdafruitDHT.py 11 4

## Slide 18
#3–1 Sensor Data Capture and Transfer: Sensor Data capture code
Install dependencies at RPi
  $ sudo apt-get update
  $ sudo apt-get install libpython3.6-dev python3-numpy
  $ sudo apt-get install mercurial
Open Sensor Data Capture code and Change IP Address
  $ vi ~/SmartX-mini/IoT-Labs/RPI_capture.py

## Slide 19
Open Sensor Data Capture code and Change IP Address
  $ vi ~/SmartX-mini/IoT-Labs/RPI_transfer.py
#3–2 Sensor Data Capture and Transfer: Sensor Data transfer code

## Slide 20
At the Docker container in NUC (Webserver)
  $ cd ~/SmartX-mini/IoT-labs
  $ nodejs webserver.js
At the Laptop (Tower)
  Open Web browser and go to http://<IP_of_NUC>
At the Rpi (Sensor Data Capture and Transfer)
  $ cd ~/SmartX-mini/IoT-labs
  $ chmod +x process.sh
  $ sudo ./process.sh
#4 Execute IoT Web service

## Slide 21
Review

## Slide 22
Lab Summary
With IoT Lab, you have experimented
An example-based realization of container-based IoT-Cloud services that can sense and actuate distributed IoT devices (i.e., Boxes).
For the cloud side, the required Web-app server realization is supported by utilizing Node.js programming.

## Slide 23
Thank You for Your Attention
Any Questions?
mini@smartx.kr